## Slide 1: Designing with High Speed Interfaces Debugging techniques and design considerations
Francesco Contu
HS and RF System Solution Expert EMEA

## Slide 2: Agenda
Introduction
TX emphasis
RX linear equalizer
RX DFE
AMD Transceiver tools
IBERT demo

## Slide 3: MGT history
First devices appeared around 2000
Mainly dictated by 10G Ethernet and STM16
NRZ encoding, Speed up to 3.125 Gbits, limited equalization
Quickly evolved to 10 Gbit/s around 2005
Sophisticated and automatic equalizers, eye scan features
PAM4 appeared around 2015 for speed > 40 Gbit/s
Again dictated by 400G Ethernet
Commercially available devices today:
NRZ 32 Gbit/s
PAM4 112 Gbit/s

## Slide 4: AMD Transceiver Block Diagram
TX Driver
Pre-emphasis
RX
DiffAmp
RX
Linear EQ
RX
DFE
SIPO
PISO
FPGA Fabric
Serial
Channel
Serial Transceiver
Hard
PCS
Logic
RX
CDR
Fully adapting
>25 db
PLL
Low Jitter
3-tap FIR
Fully adapting
> 9dB
2-D Eye Scan
Non-Destructive
High Resolution

## Slide 5: What is equalization and why it is needed
We transmit a signal S(f) over a media
    f = frequency
    Media can be copper, fiber optics, air...
The media has a transfer function H(f)
    The signal gets attenuated and distorted
We receive S(f)H(f) while we would like to get S(f)
So we need to add a module that implements 1/H(f)
    This is an ideal equalizer
S(f)H(f)(1/H(f)) = S(f)
So equalization is a passive or active circuit that corrects media attenaution and distortion, and it is needed to obtain the transmitted signal again

## Slide 6: A typical media: the Backplane
A backplane is a PCB board that connects connectors so that each pin on each connector is linked to the same relative pin on the other connector(s) forming a data bus.
(1) Silicon Transceiver
(2) TX Package TP(f)
(3) TX Line Card TL(f)
(4) TX Connector TC(f)
(5) Backplane B(f)
(9) Silicon Transceiver
(8) RX Package RP(f)
(7) RX Line Card RL(f)
(6) RX Connector RC(f)
H(f) = TP(f)TL(f)TC(f)B(f)RC(f)RL(f)RP(f)

## Slide 7: Layout discontinuities
Attenuation is only a small piece of the story
Vias, Connectors, P/N impairements, pads all generate discontinuities
Significantly contribute to distort the signal
Problem start to be very serious around 10 Gbit/s
5mil trace
28mil pad
jog-out
Two 45-degree turns
Plane cut-outs

## Slide 8: Inter-Symbol-Interference and Equalization
Inter-Symbol-Interference (ISI)
  An impulse response through a channel can expand to other symbols hence impact the waveforms at other symbols
Equalization - Mitigate ISI to ensure correct data sampling
Ideal 01000
Real 01000
UI Delayed 010s
011110
010110

## Slide 9: Equalization techniques
TX Emphasis
    Predistorts TX to anticipate channel losses
RX linear equalizer
    Compensates Channel Losses trying to implement 1/H(f)
RX non linear digital equalizer
    AKA Decision Feedback Equalizer
    Compensates intersimbolyc interference

## Slide 10: TX Emphasis

## Slide 11: TX Emphasis To Reduce Loss
Transmitted Pulses
Received Pulses
Time
Amplitude
Time

## Slide 12: TX Emphasis To Reduce Loss
Transmitted Pulses
Received Pulses
Time
Amplitude
Time
Cursor (tap #1)

## Slide 13: TX Emphasis To Reduce Loss
Transmitted Pulses
Received Pulses
Degraded Pulse
Time
Amplitude
Time
Cursor (tap #1)

## Slide 14: TX Emphasis To Reduce Loss
Pre-cursor (tap #2)
Transmitted Pulses
Received Pulses
Degraded Pulse
Time
Amplitude
Time
Cursor (tap #1)

## Slide 15: TX Emphasis To Reduce Loss
Pre-cursor (tap #2)
Transmitted Pulses
Received Pulses
Degraded Pulse
Pre-cursor
Time
Amplitude
Time
Cursor (tap #1)

## Slide 16: TX Emphasis To Reduce Loss
Post-cursor (tap #3)
Pre-cursor (tap #2)
Transmitted Pulses
Received Pulses
Degraded Pulse
Pre-cursor
Time
Amplitude
Time
Cursor (tap #1)

## Slide 17: TX Emphasis To Reduce Loss
Post-cursor (tap #3)
Pre-cursor (tap #2)
Transmitted Pulses
Received Pulses
Degraded Pulse
Pre-cursor
Post- cursor
Time
Amplitude
Time
Cursor (tap #1)

## Slide 18: TX Emphasis To Reduce Loss
Cursor (composite)
Post-cursor (tap #3)
Pre-cursor (tap #2)
Transmitted Pulses
Received Pulses
Degraded Pulse
Pre-cursor
Post- cursor
Time
Amplitude
Time
Cursor (tap #1)

## Slide 19: TX Emphasis To Reduce Loss
Cursor (composite)
Post-cursor (tap #3)
Pre-cursor (tap #2)
Transmitted Pulses
Received Pulses
Degraded Pulse
Pre-cursor
Improved Pulse
Post- cursor
Time
Amplitude
Time
Cursor (tap #1)

## Slide 20: TX Emphasis side effects
Higher TX power
Higher spectral content
Higher Xtalk
Higher sensitivity to layout discontinuities
    Vias, Connectors, any impedance change
  Manual Process

## Slide 21: RX Linear Equalizer

## Slide 22: RX Linear Equalization – Loss Compensation
No equalization
Full equalization
Channel Loss
CTLE
Combined Frequency response
+
=>

## Slide 23: Linear Equalization
  Receiver: Boosts high frequency
  Compensate insertion loss
  Can be tweaked manually or automatically
    Automatic introduced with AMD 7 Series
  Limitation: Boost high frequency noise, including Xtalk
  Recommended for:
    Repetitive patterns
      Example: GEthernet with lots of interframe gaps
    <10 db attenuation
    Clean channels (low noise, low Xtalk)
    Good return loss <-10 db
RX linear equalizer frequency response

## Slide 24: Decision Feedback Equalizer

## Slide 25: Decision Feedback Equalization
  A nonlinear equalizer that uses previous symbols to eliminate the Inter-Symbol-Interference (ISI) on current symbol.
    The ISI on current symbol, caused by previous symbols, is subtracted by DFE.
Slicer for Decision
Unit Delay
Adder to Feedback
Multiplier
Tap Weight
Z-1
Z-1
Z-1
X
W[3]
X
W[2]
X
W[1]
+
RX
X
W[n]
y(t)
yd(t)
u(t)
Equalized output

## Slide 26: DFE pros and cons
Tap weight
    Can be set automatically
    Adaptation algorithms are well known
    Hard to set manually
Automatic algorithm
    Works best with scrambled data streams
    Can be fooled by long repetitions of the same pattern
    Worst case is “10101010”
    Freezing the taps in this case solves the issue
Error propagation
    Unlikely to happen, yet possible
Does NOT amplify noise
    Best solution for noisy channels
    Main reason why it works better than Linear equalizers in a real system
Tap weight based on ISI

## Slide 27: DFE Effect

## Slide 28: Equalizer reset
AMD has automatic equalizers since the 7 Series introduction
Excellent performance and dynamic adaptation
Require reset in case of LOS (Loss Of Signal)
Without reset, the equalizer might converge suboptimally

## Slide 29: AMD Transceiver Tools: GT Wizard

## Slide 30: F.F.F.: Frequently Forgotten Feature
You MUST set the equalizer accordingly to your board attenuation
#1 source of non working designs
Defaults to 20 dbs
    Overkill for most designs
    Translates into DFE
    Not good for most 8b/10b applications

## Slide 31: AMD Transceiver Tools: IBERT and In-system IBERT

## Slide 32: System Analysis with Eye Scan Non-Destructive On-Chip Debug
Internal Scan History in Xilinx
  Multi-generations of 1-D BER plot
  From Gen 4 to Gen 6
Two Samplers in RX Path
  Data Sampler at the eye center
  Moveable Offset Sampler
  Compare two samplers
  2-D BER Eye built from error location
Eye Scan inside receiver on live data
  Non-destructive
  Post equalization
  BER Measurement
  2-D Plot
  Pattern agnostic

## Slide 33: In-System IBERT (yet another F.F.F.)
Eye Scan, Equalizer selection and TX tuning
All directly from your own design
Easily added from the GT Wizard and included in the example design
Available as an add-on IP as well
Ultrascale IP
Some XAPP exists for 7 series
Versal has it in HW automatically

## Slide 34: Power and Clocking
It is critically important to satisfy the AMD requirements in terms of power and clocking
Max power noise is normally reported in the PCB design user guide
Required Clock Phase Noise is in the DS or in Answer Records (for older families)
Very often a clock out of spec results in a GT which works looped back
It may also work when connected to a GT making use of the same clock

## Slide 35: Clocking solutions
Silica has multiple clocking solutions from timing market leaders
Clock distribution, cleanup and Generation
PLLs up to 18 Ghz
Best in class TCXO and OCXO with leading Temperature and Vibration stability
Quartz and MEMS based

## Slide 36: IBERT demo

## Slide 37: Thank you! Questions?